TSC-30 CRAWLER DRILLING RIG

Technical description

TSC-30 crawler drilling rig adopt international advantaged technology. Strict testing has been passed in the worst terrain and mountain areas. It can be used in mountain, hill, Plain, Forest, Farmland for petroleum prospecting. All of operation handles and indicators were installed on operation platform. The rig was installed with safety, caution and environmental protection symbols, and it meets with the requirement of HSE. The rig is a kind of high efficiency and applied equipment for petroleum seismic crew.

The rig includes two sections: The first section is the main-rig section in which the rotarying and pulldown of the rig is realized by an engine driving a hydraulic pump via belt. The second section is the crawler. The rig is mounted on the crawler.

The drilling rig can be work at -40℃ and +55℃, 0-3000m height above sea level, ambient temperature in dusty environment.

Main specifications

| Drilling method | Auger drilling |
| --- | --- |
| Drilling depth | Auger drilling | 15-20m |
| Drilling hole diameter |  | 80mm |
| Drilling pipe | Diameter× Length | Φ42×80×1000mm |
| Power swivel | Rated torque | more than 700N.m |
|  | Rotation speed range | 0-130r/min |
| Pulldown & hoisting system | Pull up & pull down capacity | More than 1200kg |
| Hydraulic system | Working pressure | 18MPa |
| Engine | Output power | 25-35hp/3600r/min (Gasoline engine) |
| Crawler dimensions | 2000×1600×500mm |
| Crawler weight | About 500kg or more |
| Crawler control | manual |
| Crawler speed | 0-18km or 3.4km per hour |
| Total weight | Crawler and rig ≤2000kg |