# TSP-40 Man Portable Drilling Rig

# Technical description for TSP-40 man portable drilling rig

# TSP-40 MAN PORTABLE DRILLING RIG

# Technical description for TSP-40 man portable drilling rig

TSP-40 man portable drilling rig was designed in 2003 and adopted international advantaged technology. Strict testing has been passed in the worst terrain and mountain areas. It can be used in mountain, hill, Plain, Forest, Farmland for petroleum prospecting. All of operation handles and indicators were installed on operation platform. The rig was installed with safety, caution and environmental protection symbols, and it meets with the requirement of HSE. The rig is a kind of high efficiency and applied equipment for petroleum seismic crew. The rig can be disassembly into 6 modules, and each module weight was not exceed 75kg.

The rig has the advantages of light-weight, simple construction, easy to assemble, disassemble, transport and operate.

The drilling rig can be work at -10℃and +55℃, 0-3000m height above sea level, ambient temperature in dusty environment.

# Main specifications

| Drilling method | Air hammer drilling |
| --- | --- |
|  | Air drilling |
| Drilling depth | Air hammer drilling | 40 m |
|  | Air drilling |  |
| Drilling hole diameter |  | 80mm |
| Drilling pipe | Diameter X Length | Φ60X1500mm (Air drilling pipe) |
| Power swivel | Rated torque | 1300N.m |
|  | Rotation speed range | 0-150r/min |
| Pulldown & hoisting system | Pull up & pull down capacity | 2000kg |
|  | Pulldown force | 5.5kN |
|  | Max hoisting speed | 0.73m/s |
| Hydraulic system | Working pressure | 20MPa |
| Engine | Output power | 25hp/3600r/min, (Gasoline engine) |
| Weight of each module |  | ≤75kg |
| Total weight |  | ≤330kg |